## Slide 1
Resistivity and Resistance
Resistivity is a property of a material describing the degree to which the material opposes the flow of charges through the material.
Resistance is a property of a device describing the degree to which the device opposes the flow of charges through the device.

## Slide 2
Resistivity
Resistivity depends on material properties that are mostly beyond the scope of this course.
Resistivity for a few common materials:
Material Resistivity, ρ (Ωm)
Silver 1.59 x 10-8
Copper 1.68 x 10-8
Gold 2.44 x 10-8
Aluminum 2.65 x 10-8
Silicon 6.40 x 102
De-Ionized Water 1.80 x 105
Diamond 1.00 x 1012

## Slide 3
Resistivity
Resistivity depends on temperature. The temperature dependence is particularly important for conductors.
Material Resistivity, ρ (Ωm) α (K-1)
Silver 1.59 x 10-8 0.0038
Copper 1.68 x 10-8 0.0040
Gold 2.44 x 10-8 0.0034
Aluminum 2.65 x 10-8 0.0039
Silicon 6.40 x 102
De-Ionized Water 1.80 x 105
Diamond 1.00 x 1012

## Slide 4
Resistance
Resistance depends on the material (resistivity) and the geometry of the device.
Resistance is proportional to device length and
inversely proportional to cross-sectional area.

## Slide 5
Resistance
Resistance depends on the material (resistivity) and the geometry of the device.
(If the cross-section is not uniform throughout the length of the device, one must integrate to determine R.)
y
x
z

## Slide 6
Resistance
Consider connecting two resistors of the same cross-sectional area in series.

## Slide 7
Resistance
Consider connecting two resistors of the same length in parallel.

## Slide 8
Quantity | Series | Parallel
Capacitance |  | 
Resistance |  | 
Potential Difference |  | 
Current |  | 
Charge on Capacitor |  | 
Circuits

## Slide 9
Quantity | Series | Parallel
Capacitance |  | 
Resistance |  | 
Potential Difference |  | 
Current |  | 
Charge on Capacitor |  | 
Circuits
OSE’s